Supplement

Outline
1. Splicing commitment model – time delay implementation
1.1. Model topology
1.2. Numerical simulation
1.3 Relationship between gene structure, time delays and polymerase speed
1.4 Analytical solution
2. Splicing commitment model – multistep implementation
3. Mechanistic exon definition model
4. Stochastic simulations
5. Supplemental Tables with parameter values

# 1. Splicing commitment model - time delay implementation
## 1.1 Model topology

In Figs. 1, 2 and 5A-C, we performed simulations using the splicing commitment or time delay model, in which we describe the splicing fate of a transcript during its synthesis and consider splicing reactions that eventually occur with delays.

We implemented a system of four ordinary differential equations (ODEs) describing unspliced transcripts (“mRNA”), spliced transcript with the alternative exon included (“Incl”) or skipped (“Skip”) and inhibited mRNA (“mRNAinh”), in which the unspliced mRNA is bound by an inhibitory RBP and inclusion is no longer possible (Fig. 1B).

\begin{align*} \frac{d}{d t} mRNA &= - mRNA \cdot \left(kesc + ki + ks\right)\\ \frac{d}{d t} Incl &= ki \cdot mRNA\\ \frac{d}{d t} Skip &= ks \cdot \left(mRNA + mRNAinh\right)\\ \frac{d}{d t} mRNAinh &= kesc \cdot mRNA - ks \cdot mRNAinh\\ \end{align}	(Equation 1)

All splicing commitment reactions are assumed to irreversible and occur with the parameters ki (inclusion), ks (skipping) and kesc (inhibitor-mediated commitment to skipping). To implement co-transcriptional splicing, we consider that splicing commitment reactions can occur after different delay times (see below), and chose these delay times based on known molecular mechanisms of splicing. Specifically, we assumed an exon definition mechanism which is known to apply for most splicing events in human cells (REF). In exon definition, not only the spliced intron, but also the flanking exons need to be fully recognized by the spliceosome for intron splicing to occur. Hence, during transcript elongation, splicing of the first and second intron is only possible after synthesis of exon 2 and 3 is complete, respectively.

For, simplicity, we neglect the initial, splicing-less phase before exon 2 is fully synthesized (State P0 in Fig. 1B), and model only the transcript fate afterwards (State P1 in Fig. 1B). In terms of splicing commitment, exon inclusion is immediately possible after start of the simulation, whereas skipping can only occur only later, once both introns and all exons have been synthesized (States P7-P8 in Fig. 1B). To implement the time shift of skipping relative to inclusion, we did not explicitly model polymerase progression, but considered a time delay τ for the skipping reaction (Fig. 1C, “time delay model”). Specifically, the rate of commitment to skipping (kS) is initially zero and then increases in a step-like manner, whereas the commitment rate to inclusion (ki) is time-invariant.

## 1.2 Numerical simulation
To numerically implement these time delays, we performed our simulations in several consecutive simulation steps, each of which represents the interval between two time delays. The simulation starts at time t=0 (completion of exon 2 synthesis, see above) and we set all species to zero, except for the unspliced mRNA, which we assume to be 1. Thus, we assume a synchronized population of mRNA molecules (100% just elongated through exon 2), and will use the numerical simulation routine described below to calculate the relative probability to end up in a certain splicing fate.

To do so, the ODE system is initially integrated until the first time delay using ODE solver xxx from zzz. In Fig. 1C and D, no skipping can occur in this first time phase (ks = 0), and inhibitor-mediated skipping does not occur (kesc = 0). Thus, the ODE system reduces to:
\begin{align*} \frac{d}{d t} mRNA &= - ki \cdot mRNA \\ \frac{d}{d t} Incl &= ki \cdot mRNA\\ \end{align}	(Equation 2)

The integrals of the simulated mRNA and Incl time courses represent the likelihood of a transcript to be unspliced or spliced to inclusion until the time delay τ, i.e., until exon 3 is fully synthesized. To determine the final fate of all transcripts, we continue the simulation for t > τ, now considering that skipping is possible.
\begin{align*} \frac{d}{d t} mRNA &= - mRNA \cdot \left(kesc + ki \right)\\ \frac{d}{d t} Incl &= ki \cdot mRNA\\ \frac{d}{d t} mRNAinh &= kesc \cdot mRNA \\ \end{align}	(Equation 3)

Please modify the ODE system
The initial value vector of species in this second time phase is the final species from the first integration step (Eq. 2) at the end time point t = τ. The simulation is performed till the unspliced mRNA species approaches zero, i.e., until all molecules are spliced. Then, the time courses of the first and second time steps are merged and integrals are calculated to determine the probability of skipping and inclusion.
Equations:
P(Incl) = Integral(Incl)t=0-inf
## P(Skip) = Integral(Skip)t=0-inf
## Then, alternative splicing is quantified using the PSI metric, which equals the probability of inclusion.
## PSI = P(incl) / (P(Incl) + P(Skip)) = P(Incl)
## In Fig. 2, the RBP inhibitor prevents inclusion and this is implemented using the “escape” reaction kesc which results in early transcript commitment to skipping. It is assumed that inhibitor binding and early skipping commitment can occur in a restricted time window between the delays tauinh,1 and tauinh,2. Thus, when considering this inhibitor-mediated skipping, the number of integration steps increases to four (e.g., t0 → tauinh1; tauninh1 →tauninh2, tauninh2 → tau, tau → infinity)
## 1.3 Relationship between gene structure, time delays and polymerase speed
## To be completed - hier wuerde ich die Gleichungen, die frueher im Bild waren, einfuehren und alle Groessen erklaeren.
## 1.4 Analytical solution
The approach for calculation the analytical solution for PSI of multistep models is based on the probability for the inclusion reaction. Under the assumption that the simulation starts with one molecule of mRNA one can calculate the probability of inclusion reaction for each of the four time phases dt1, dt2, dt3, dt4 (Fig. 1).
The first step is the calculation of p1 representing the probability for inclusion within the first phase dt1. Assuming a poisson process we can calculate the expected value A1=k1*dt1 , showing the amount of expected inclusion reactions whitin the phase 1. Considering exponential distribution we get p1\in[0,1] as the value from cumulative distribution function:

Illustration 1: Schematic representation of analytical solution approach. At the top is the step model we are originating from. In the middle is the parameter time course of the derived time delay model. The analytical approach is based on this model (bottom). p1-p4 are absolute probabilities for inclusion reaction in the corresponding phases 1-4.

p_1 = 1 - e^{- A1}	(Equation 4)

The probability that a reaction won't take place in the first phase is p_{rest1} = p - p_1 . The general formula for rest/remaining probability after the phase i is:

p_{rest_{i+1}} = p_{rest_i}*(1 - p_{react_i})	(Equation 5)

In the second phase there are two competing reactions. The expected value for both reactions is A2+A3 = (k_{esc} + ki )* dt2 . The probability for one of the reaction will occur is p_{react_2} = 1- e^{-(A1 + A2)} . The probability for inclusion reaction results from:

p_2 = p_{react_2}*\frac{A2}{A1 + A2} = p_{react_2}*\frac{ki}{ki + k_{esc}}	(Equation 6)

Consequently the rest probability for phase 3 is p_{rest_3} = p_{rest_1}*(1-p_{react_2}) .

For the two remaining phases we can proceed in the same manner. Eventually we get the PSI-value as a sum of all absolute probabilities for inclusion p1-p4:
PSI = p_{incl} = \sum_{i=1}^{4}p_i	(Equation 7)

# 2. Splicing commitment model - time delay implementation

Ich bin nicht sicher, wie Du hier gerechnet hast – ich war eigentlich davon ausgegangen, dass hier “ganz normal” ODEs simuliert werden, also ein System mit konstanter p1-Synthese und gleicher Degradation (1. Ordnung) fuer alle Spezies. Auch bei einer unsynchronisierten Simulationen (alle Spezies initial null) wuerde sich hier ein Steady State einspielen und der Delay ist intrinsisch durch die vielen Schritte fuer jedes Molekuel “eingebaut”. Das waere eigentlich der Weg gewesen, wie ich das Problem implementiert haette (oder ueber wesentlich kompliziertere Delay Differentialgleichungen, wo jedes Molekuel wiederum sein eigenes Alter bekommt). Das war im Bello-Modell auch so implementiert und so denken eben viele ODE-Leute (also die Mass der Modellierer). Du scheinst es aber aehnlich dem time delay modell implementiert zu haben, nur dass die Schritte der Delay sind (?). Aus Zeitgruenden lassen wir es dann jetzt mal so, muessen aber das andere uU in einer Revision machen. Du muesstest die Beschreibung hier moeglichst kurz ergaenzen, aehnlich wie in Section 1, also wie wurde simuliert (Initialbedingung; Solver), Was ist der PSI, wie wurde vpol berechnet, wo fliesst kesc ein?

To verify the time delay implementation (Section 1), we also performed more convent The ODE system for the step model from the same chapter looks like the following:

\begin{align*} \frac{d}{d t} p_{1} &= - p_{1} \cdot \left(k_{elong} + ki\right)\\ \frac{d}{d t} Incl &= ki \cdot \left(p_{1} + p_{2} + p_{3} + p_{4} + p_{5} + p_{6} + p_{7} + p_{8}\right)\\ \frac{d}{d t} Skip &= ks \cdot \left(e_{7} + e_{8} + p_{7} + p_{8}\right)\\ \frac{d}{d t} p_{2} &= k_{elong} \cdot p_{1} - k_{elong} \cdot p_{2} - ki \cdot p_{2}\\ \frac{d}{d t} p_{3} &= k_{elong} \cdot p_{2} - k_{elong} \cdot p_{3} - ki \cdot p_{3}\\ \frac{d}{d t} p_{4} &= k_{elong} \cdot p_{3} - k_{elong} \cdot p_{4} - ki \cdot p_{4}\\ \frac{d}{d t} p_{5} &= k_{elong} \cdot p_{4} - k_{elong} \cdot p_{5} - ki \cdot p_{5}\\ \frac{d}{d t} p_{6} &= k_{elong} \cdot p_{5} - k_{elong} \cdot p_{6} - ki \cdot p_{6}\\ \frac{d}{d t} p_{7} &= k_{elong} \cdot p_{6} - k_{elong} \cdot p_{7} - ki \cdot p_{7} - ks \cdot p_{7}\\ \frac{d}{d t} p_{8} &= k_{elong} \cdot p_{7} - ki \cdot p_{8} - ks \cdot p_{8}\\ \frac{d}{d t} e_{7} &= - e_{7} \cdot ks\\ \frac{d}{d t} e_{8} &= - e_{8} \cdot ks\\ \end{align}	(Equation 1)

For integrating/solving the System of given ODEs we use the function odeint from the python package scipy. (https://docs.scipy.org/doc/scipy/reference/generated/scipy.integrate.odeint.html). The result is the time course of all species.

# 3. Mechanistic exon definition model
Text unten ist aus dem Haupttext einkopiert, also nicht final

Ich schlage folgende Gliederung vor

1) Short introduction: Motivation, Which figures were simulated with this model?

2) Model topology (Equations and their meaning)

3) Numerical simulations – evtl kein eigener Abschnitt werden – du kannst wohl auf Section 1 verweisen, musst nur sagen, wodurch nun die Delays entstehen;
-alle Exon-Enden sind ein Delay\
-t=0 ist wirklich Start des Transkripts;
-Ende des Transkripts schaltet Retention an und wieso ist das so angenommen

4) Spatial range RBP-mediated inhibition: Was genau sind die Inhibitionsfunktionen in Fig. 4 (Gleichungen)

To explicitly model binding of the inhibitory RBP to the pre-mRNA, we turned to mechanistic modeling. Specifically, we considered RBP binding to the pre-mRNA, assumed that the RBP inhibits nearby splice sites and considered that introns may be retained if splicing becomes inefficient.

This mechanistic model was based on our previous work on exon definition, in which we modeled recruitment of pioneering spliceosome U1 and U2 subunits to splice sites (Fig. 3A and Enculescu et al., 2020). Specifically, we considered that all three exons may be “defined” by cooperative U1 and U2 binding across exons. Initially, the pre-mRNA is synthesized as an unbound precursor (P000), and then irreversible exon definition may occur in a combinatorial fashion with the rate constants k1-k3 (Fig. 3A, left). For instance, the both outer exons are defined in the states P101 and P111, whereas the middle exon is either undefined (P101) or defined (P111). These spliceosome binding patterns impact on splicing outcomes, as we assume splicing reactions (kspl) to inclusion (state P111), skipping (P101) or retention (all other states).

As depicted in Fig. 3A (right), the inhibitory RBP modulates splicing outcomes by irreversibly binding to all unspliced pre-mRNA states (e.g., P000P000_inh). Subsequently, spliceosome binding occurs at reduced rates (k1,inh-k3,inh), but splicing rates (kspl) remain unchanged. Thus, the inhibitory RBP changes splicing outcomes by blocking initial spliceosome recruitment. Importantly, this occurs only locally around the sites of RBP binding, i.e., around an assumed RBP motif (Fig. 3B; vertical dashed line). For simplicity, we initially assumed a bell-shaped inhibition profile, in which the RBP effects on k1-k3 decay within ~100 bp around the binding site. Consequently, when binding with sufficiently short introns, the RBP can simultaneously affect the definition of two exons as schematically depicted in Fig. 3B.

Co-transcriptional spliceosome binding and splicing were considered in the model by assuming that an exon can only be defined just after its synthesis is complete. Hence, the rate constants k1-k3 and k1,inh-k3,inh change in a time-dependent manner after transcript initiation and increase in a step-like manner with delays that reflect the relative positions of exons within the pre-mRNA (Fig. 3C). For the RBP, we again assumed RNA polymerase-dependent recruitment, and therefore modeled RBP binding as a short window-of-opportunity, reflecting the phase when the elongating enzymes passes the RBP motif.

# 4. Stochastic simulations
1) Introduction

To quantify uncertainties in splicing outcomes, we performed stochastic simulations using our co-transcriptional splicing models and compared all previously introduced model variants…..

2) Implementation: Hier muss beschrieben werden, wie Du das gemacht hast. Also Gillespie bestimmt ja erstmal, wann die naechste Rkt stattfindet (e-Fkt) und dann welche (aus den Probabilities) – so zumindest meine Erinnerung.... Ich denke, du hast einfach alle Events gesampelt und geguckt, welches als erstes stattfindet, oder? So hatte ich es im Gruppentreffen verstanden. Ich denke, es laeuft auf das gleiche raus, muss aber beschrieben werden. Wenn Du doch nur Gillespie benutzt hast, musst du das Package erwaehnen und ausserdem wuerde ich der Reproduzierbarkeit alle Reaktionen einzeln auflisten. Wie wurden die Reaktionswahrscheinlichkeiten bestimmt – da es nur Reaktionen erster Ordnung sind, kann man sie mit den kinetischen Parametern im ODE-Modell gleichsetzen, oder?

For stochastic simulations, delay times, commitment rates and inhibitor/spliceosome binding rates to mRNA were sampled from exponential distributions to determine the order of reaction steps in a manner reminiscent of the Gillespie algorithm (Supplement). This way, we take into account stochastic variation in transcript elongation (delay times) and biochemical steps of splicing decision making. The stochastic simulation was repeated xxx times for each parameter combination and the PSI metric was calculated to obtain splicing distributions across xxx cells (Fig. 5A).

3) Evtl Details zum Vergleich mit der binomialen Verteilung? Wieso wurden die Modelle unterschiedlich behandelt?